## Slide 1: INTELLIGENT SUSTAINABLE LIVEABLE BUILDINGS FOR THE 21ST CENTURY
DEREK CLEMENTS-CROOME
UNIVERSITY OF READING
INTELLIGENT BUILDINGS INTERNATIONAL
WWW.DEREKCROOME.COM
2024

## Slide 2: DAXIA PLANT FILLED TOWER XIAN by ZAHA HADID ARCHITECTS 210m

## Slide 4: DAXIA TOWER XIAN
Cascades of plant terraces to clean air and promote wellbeing
Views out for all occupants
LEED Gold
Rainwater capture
Solar Panels
Advanced smart measurement systems with analytics

## Slide 5: Terminology

## Slide 6: ORIGINS and LESSONS for INTELLIGENT BUILDINGS
HISTORY
NATURE
TECHNOLOGY
BUILDINGS FOR HUMANITY

## Slide 7: LESSONS FROM HISTORY: VERNACULAR ARCHITECTURE

## Slide 8
Behling 1996

## Slide 9
THERMAL PERFORMANCE OF THE IGLOO

## Slide 10
Wind towers in Yazd, Iran to ventilate houses, are also constructed to cool underground cisterns.
Ice House at Kerman Iran. Ice formed during frosty winter nights in the shallow channels protected from the sun’s rays by the high wall. Its packed between layers of straw in the mud-brick dome.
Michell 1978

## Slide 12: The J.M Tjibaou Cultural Center (Museum of Noumea)
Designed by Renzo Piano (Winner of 1998 Pritzker prize), is a harmonious alliance of modern and traditional Kanak architecture. Traditional thatch huts, native to the Kanak people, inspired the design.
Piano learnt from local culture, buildings and Nature. Tall thin curved laminated iroko wood ribbed structures supported by steel ties resist cyclones and earthquakes. The ribs have horizontal slats which allow passive environmental control to occur. The slats open and close according to wind strength and direction and admit air to a cavity which is linked to the glazed façade of the museum.

## Slide 15: Buildings, Environment & People
Occupant
Observer / passer by
External environment
Building
Internal environment

## Slide 16: Integration
People
Product
(Systems)
Process

## Slide 17: INTEGRATING ?
WHAT?
IDEAS
VISIONS
STRATEGY
TACTICS
HOW?
HISTORY/ NATURE/TECHNOLOGY
PROCESSES
DISCIPLINES WTHIN and WITHOUT

## Slide 18: Sustainable Design Adds Value

## Slide 19: LEED Rated Buildings
Hirigoyen (2009) ;Bernstein and Russo (2010)
cost 6% more to build; but with integrated design maybe 0%
have occupancy rates over 4% higher;
command 2-6% higher rents;
save 10-50% in energy consumption;
decreased operating costs;
increased building value 10% in 2008

## Slide 20: PEOPLE

## Slide 21: DESIGN
Humanity
Utility and
Sensory Beauty

## Slide 22: MIND and BODY

## Slide 23: WELL STANDARD v2 2018
BASED ON US INPUTS FROM STAKEHOLDERS AND MEDICS
AIR
WATER
LIGHT
COMFORT
MIND
SOUND
MATERIALS
COMMUNITY
NOURISHMENT
FITNESS

## Slide 24: Impact of WELL Certified Buildings
See paper by Nasim Ildiri et al., in Journal Building and Environment vol 224, 2022, 109539, doi: 10.1016
Improves health and wellbeing
1300 POE responses

## Slide 25: Beyond Environmental Comfort
Clements-Croome 2020 Designing Buildings for People

## Slide 27
Saves Energy
Care
of People
Leaner and Fresher
Environments
Greener

## Slide 28: LESSONS FROM NATURE

## Slide 29: Characteristics of Nature
Benyus (2002)
runs on sunlight;
uses only the energy it needs;
fits form to function;
recycles;
rewards cooperation;
banks on diversity;
demands local expertise;
realises the power of limits.

## Slide 30: Organic Architecture
Organic architecture promotes harmony between human habitation and the natural world through design. Sympathetic and integrated into its site so that buildings, furnishings, and surroundings become part of a unified, interrelated composition.
Fallingwater by Frank Lloyd Wright

## Slide 31: SPIDERS WEBS

## Slide 32
Eastgate Office Building in Harare Zimbabwe inspired by termites nest

## Slide 34
The camel's nose acts as both a humidifier and a dehumidifier with every breathing cycle.
The hot, dry air that is inhaled passes over the large area of moist membrane. This air is immediately humidified by picking up moisture from the nose and cooled in the process,. This cooler air passes to the lungs and remains at approximately body temperature.
When it is exhaled, it is cooled even further by passing over the same nasal membranes, this time by a process of dehumidifying instead of humidifying. The nasal membranes are coated with a special water-absorbing substance that extracts the moisture from the air like the cooling coils of a dehumidifier.
A net savings of 68 percent in the water usually lost through respiration occurs just between the cooling and drying phases of the breathing cycle.

## Slide 35: Alberto Estévez’s Bioluminescent Tree
Experiments in bio-illumination with implications for architecture, industrial and environmental design.
Dollens, 2005,Design Biomimetics: An Inquiry and Proposal for Architecture and Industrial Design

## Slide 36: Benefits of Biophilia
Nature enhances health and wellbeing
Increased physical activity
Reducing harmful exposures,
Increases social engagement
Improves mental health
Off-sets Heat Island Effect
Green landscaping may help climate change in regards CO2, temperature……
Green vegetation associated with decreased mortality (Harris et al Harvard 2016)

## Slide 37: Technology Hype Cycle
New technologies are over hyped by the media and businesses.
A hype cycle is a graphic representation of the maturity, adoption and business application of specific technologies.

## Slide 38: Significant Technologies
AI
Robotics (manufacturing and maintenance)
New materials
3D, 4D printing
Virtual and Augmented reality
Internet of Things (eg Wearable technologies)
Biophilic Design

## Slide 39: Airconditioning without Electricity
Photonics uses coatings which reflect solar radiation but also emits the infra- red from the inside of the room and thus effects cooling without airconditioning.
Multi-layered films of hafnium oxide and silicon dioxide reflect 97% of sunlight at wavelengths of 8—13 micro metres. This results in the temperatures of such film coated surfaces being about 5 deg C below other surfaces. Cooling power is about 40W/m2
(Nature 27 November 27 2014 volume 515 page 541 by A P Raman et al.,Stanford University).

## Slide 40: GRAPHENE
Carbon atomic scale honeycomb lattice
Lightest strongest and stiffest substance known
Can self-repair
Many applications
Look our for Phospherine

## Slide 41
Oculus Rift & Mindwave
Notes: Image: Arup Associate © So Hyun
Reference:
http://raconteur.net/business/robots-virtual-reality-and-wearable-tech-set-to-enter-the-workplace
http://www.information-age.com/technology/applications-and-development/123460817/augmented-reality-and-wearable-tech-marriage-made-enterprise

## Slide 42: SENSORY WORLD Embedded Sensors in Buildings, Equipment, Clothing and the Body

## Slide 43: CARBON POSITIVE BUILDINGS
Artificial Leaf can generate hydrogen

## Slide 44: Hydrogen Production in Leaves

## Slide 45: Hydrogen Producing Façade
A Water Wall with Artificial Leaves Immersed Within
Sunlight Radiates Causing Reaction
Hydrogen Produced

## Slide 46: Case Studies

## Slide 47: Green Mega City: Lilypads by Vincent Callebaut
http://www.popsci.com/futurecity/plan.html

## Slide 48: Green Mega City: Lilypads by Vincent Callebaut
http://www.popsci.com/futurecity/plan.html
Titanium Dioxide skin to absorb CO2
2 seater electric pod cars
Biodiesel/electric buses guided by embedded road magnets
Footstep energy
Wind turbines using air movement
Hydrogen from an Algae Park
Tidal power from wind from passing car
Solar energy from paint containing solar nanoparticles

## Slide 49: Green Mega City: Lilypads by Vincent Callebaut
Solar energy from paint containing solar nanoparticles
Clear water from desalination
Robotic maintenance
Bubble Houses
Phase change materials give temperature regulation
Hydroponic farms
Plant water from sewage filtered via zebra mussels
10 storey concrete tower with embedded photovoltaics
Geothermal wells for heating/cooling
http://www.popsci.com/futurecity/plan.html

## Slide 50: UV PCO
Photocatalytic Oxidation (PCO) or Photocatylisis is the opposite of photosynthesis.
PCO is a natural process whereby Ultra Violet light energy reacts with the mineral Titanium Dioxide (TiO2), triggering a chemical process that safely and instantly oxidizes or breaks up organic matter at a molecular level.
As a catalyst, TiO2 continues to work and is not consumed in the process.
www.pureti.co.uk

## Slide 51: Improving Air Quality
PURETi treated surfaces work with nature to purify air quality including:
Volatile Organic Compounds (VOCs)
Smog incorporating NOx and organic Particulate Matter.
Odours from methane – such as tobacco smoke, human and agricultural waste.
Methane / Formaldehyde
Indoors on windows and lighting
Outdoors on building exteriors,
hardscapes, asphalt and concrete.
www.pureti.co.uk

## Slide 52: Phase Change Materials
The RACUS® ceiling tile incorporates a bio-based phase change material which captures and stores excess heat gains from within the building which reduces the need for air conditioning.
The phase change material is a composition of vegetable oils and fatty acids which are microencapsulated within an acrylic polymer shell that are embedded within the ceiling tile.“
"RACUS® stands for Reducing Air Conditioning Units and Systems.

## Slide 53
Microencapsulated Bio-based PCM
VEGETABLE OIL & FATTY ACID PCM CORE
ACRYLIC POLYMER SHELL

## Slide 54
28
26
24
20
18
Infra-red Thermal Imaging
19°C
Room Temp.
with RACUS®
20°C
22°C
24°C
22°C
20°C
Room Temp.
without RACUS®
24°C

## Slide 55: ATES - Aquifer Thermal Energy Storage

## Slide 60: BIQ Algae Powered Building Hamburg 2013
Bio Intelligent Quotient building by Arup/Splitterwerk £4.8m 3 years
129 Algae louvred tanks SE/SW facades
Algae +nutrients+CO2+sunlight
Algae harvested and processed for biogas
Also shades building
Solar heat used too

## Slide 62: Masdar City Abu Dhabi 2005--2025

## Slide 67: Edge Building by Deloitte 2015
28,000 sensors
Edge mobile App
Finds desk
Sitting, standing, meeting, concentration spaces
BREEAM 98.4%
LED digital ceiling with 8.3 years payback
Workspaces < 7 m from window

## Slide 68: EDGE BUILDING
Natural ventilation via atrium
1000 hot desks for 2500 workers
Breakout spaces available+ Gym
Interactive walls
Personal data not shared
Electric parking
Aquifer water storage for radiant heating-cooling
Solar panels on South face

## Slide 69: FUTURES
Carbon positive buildings like artificial leaf hydrogen generating facades also
Algae biofuel facades
Green living facades
Applications of biomimetics
Smart materials for reactive facades; embedded sensors, nanotubes , graphene
Application of nanotechnologies

## Slide 70: FUTURES
Robotics for prefabrication, cleaning, maintenance and site assembly
Fully integrated interoperable systems
Buildings into smart grid system
Wireless Sensor Technology IoT linking climate, building, systems and occupants
Innovation with respect for passive low technology and smart materials
New culture of value, systems and holistic thinking and vision

## Slide 71: THANK YOU

## Slide 74: WHAT WE CALL THE BEGINNING IS OFTEN THE END AND TO MAKE AN END IS TO MAKE A BEGINNING THE END IS WHERE WE START FROM T.S.ELIOT-- FOUR QUARTETS-- LITTLE GIDDING